## Slide 1: Project – Global Router (1)
Given a row placement result shown at the top
Superimpose global routing grids (as shown at the bottom)
Locate instance pins to be connected
Create a netlist for global router
Model Gcell (x, y) boundary capacity
  Assuming 3 metal routing layers
  M1, M3 prefer horizontal wiring
  M2 is for vertical wiring

## Slide 2: Project – Global Router (2)
M1 is pretty much occupied by cells. Only few tracks available for routing
M2 runs vertically. Need to watch out pin access, i.e., a M1 pin needs to go up to M2 first (since M1 is almost blocked)
M3 runs horizontally – serves as main routing resource
G(1,0)
G(1,3)
G(1,1)
G(1,2)
G(2,0)
G(2,3)
G(2,1)
G(2,2)
G(3,0)
G(3,3)
G(3,1)
G(3,2)
G(4,0)
G(4,3)
G(4,1)
G(4,2)
G(0,0)
G(0,3)
G(0,1)
G(0,2)
M1
M3
M2
L
B
R
T

## Slide 3: Global Routing Input Format
Please see an example on the right. For this project, please use a word doc uploaded to eeClass.
# global routing inputs
# (first character in a line means comment)
# routing_layers N layer_name its_preferred_direction // number of routing layers
# Gcell_grid number_of_Gcell_column number_of_Gcell_row
# GC (Gcell) column_index row_index L (M1 left_edge_capacity M3 edge_capacity) R right_edge_capacity B bottom_edge_capacity T top_edge_capacity
# net_name pin_at_Gcell ( x1 y1 ) ( x2 y2 ) ( x3 y3 )
routing_layers 3 M1 horizontal M2 vertical M3 horizontal
Gcell_grid 5 4
Gcell
GC 0 0 L (M1 0 M3 0) R (M1 1 M3 3) B (M2 0) T (M2 3)
GC 0 1 L (M1 0 M3 0) R (M1 1 M3 3) B (M2 3) T (M2 3)
…
nets
N1 (0 0) (1 0) (2 2)
N2 (0 1) (2 1) (4 1) (4 0) (1 2)

## Slide 4: Expected Outputs (1)
Please try to route all the nets, while trying to minimize congestions (i.e., overflow at Gcell boundaries)
For each net, you can use simple L-shape scheme, or minimum rectilinear spanning tree, or any approximation to get nets globally routed. Please find a way to draw the GR results.
  For now, ok to collapse all the routing layers to a 2D routing map
Then, highlight boundaries with supply & demand. Next is to find ways to improve to reduce congestions.
G(1,0)
G(1,3)
G(1,1)
G(1,2)
G(2,0)
G(2,3)
G(2,1)
G(2,2)
G(3,0)
G(3,3)
G(3,1)
G(3,2)
G(4,0)
G(4,3)
G(4,1)
G(4,2)
G(0,0)
G(0,3)
G(0,1)
G(0,2)
N2 (0 1) (2 1) (4 1) (4 0) (1 2)
can have the above wiring patterns:
G(0,1), G(1,1), G(1,2), G(2,1), G(3,1), G(4,1), G(4,0)
(Note: for now we collapse all the routing layers to a 2D routing map)

## Slide 5: Expected Outputs (2)
After trying your best, please show the (supply, demand) at Gcell boundaries
Then, show which boundaries have the most severe overflows
  They form a congestion map
If no enough time to complete the program, it is fine to draw your GR result by hand (but will get less points)
G(1,0)
G(1,3)
G(1,1)
G(1,2)
G(2,0)
G(2,3)
G(2,1)
G(2,2)
G(3,0)
G(3,3)
G(3,1)
G(3,2)
G(4,0)
G(4,3)
G(4,1)
G(4,2)
G(0,0)
G(0,3)
G(0,1)
G(0,2)
N2 (0 1) (2 1) (4 1) (4 0) (1 2)
can have the above wiring patterns:
G(0,1), G(1,1), G(1,2), G(2,1), G(3,1), G(4,1), G(4,0)